Nissan Skyline R33 Factory Head Unit Replacement
Written by Greg Rudakov (NS2500 on SAU) - 27th March 2003

NOTE: Use this document at own risk, if you are not confident performing this procedure seek a professional.

| Tools? | Parts? |
| --- | --- |
| Medium Phillips Head Screwdriver Wire cutters/strippers Soldering Iron & Solder Chisel (see below) | Pocket/Insert to fill gap left over (Single DIN units) - $25 @ Nissan Nissan Double Diversity Antenna adaptor (2 pin Male Japanese to Australian) - $13 @ Autobarn Terminal Blocks - $3ea @ Bunnings |

Estimated Time - 1-2 hours

Instructions...

1. Remove Ashtray

Remove ash tray and unscrew the single screw shown above.

2. Remove Gear Stick Surround

Unscrew gear-knob and remove surround by lifting it upwards.

3. Remove Console Surround

Unscrew the 2 screws holding the surround.

Remove Console Surround by lifting from bottom edge. This whole section (to the driver's door) can be lifted out enough to remove the factory stereo.

4. Remove the Factory Unit

Unscrew the 4 screws holding the factory brackets.

Remove the factory unit.

5. Wiring

Cut wiring from factory unit, strip and solder (tin) the ends. Screw into terminal blocks.

Connect unit Ground to chassis, I used this point as it already has a hole and is easily accessible. For a stronger ground consider using the larger bracket or further down towards the gearbox.

Connect factory wiring with corresponding unit wiring.

6. Mounting New Unit (in this case a JVC KD-S785)

As the JVC has a large surround (for the detachable face) I needed to redrill the mounting holes 10mm back so unit lined up properly.

The sides of the surround needed to be removed (carefully with a chisel) so as to clear the edges of the mounting bracket.

Mount the Unit back into the console using the 4 screws taken out previously.

7. Finishing Off

Replace console surround (carefully) and screw both (2) screws back in. Replace gear stick surround and screw in single screw. Put back ash tray and screw on gear-knob.

8. Done

Final Installation. Nice work